## Slide 1: Access Networks: Troubleshooting
Nick Feamster CS 6250 Fall 2011

## Slide 2: Home Networking & Access Networks
Problems
  Performance problems are difficult to debug
  Access ISPs discriminate, give poor performance
  Hard to manage, troubleshoot, secure
Research
  Programmable gateways in homes
  Perform active and passive measurements
  Collect information about user behavior
  Remotely control, troubleshoot, and secure
Notes: Home networks are difficult for experts to debug, let alone average home users. As we have recently seen in the news, the Federal Communications Commission has also taken an interest in benchmarking access ISP performance in the US, pursuing a deployment of measurement devices in more than 10,000 homes across the country to measure access network performance from various vantage points. We are collaborating with the FCC in this effort: we have analyzed a similar dataset for home network users in France and are now cooperating with the FCC to deploy programmable gateways in homes around the United States. These boxes (shown on the slide) perform a combination of active and passive measurements of both the access link, and of performance inside the home. This allows us to answer interesting questions such as: Where is the cause of performance degradation that a home user is experiencing (e.g., on the access link or inside the home)? We are also collaborating with professors in HCI (Keith Edwards) to understand user behavior (e.g., how users respond to poor performance).

## Slide 3: User Performance is Poor
Cumulative fraction of users
95th percentile of download speeds / advertised SLA
Fewer than half of the users achieve 80% of advertised SLA. Why?
S. Sundaresan, L. Di Cioccio, N. Feamster, R. Teixeira. “Which Factors Affect Home Network Performance?”

## Slide 4: We Know Very Little
User performance does not match advertised rates
We have very little idea why
  We don’t even know how many performance problems occur due to problems inside vs. outside the home
We have no idea how users react when performance suffers
Notes: Add a diagram from Beki/Keith’s networking papers

## Slide 5: Future: “User Proof” Networks
Hide complexity from the user
  Improve interfaces
Outsource management to third party
Usage model
  Users plug devices into home network gateway (or associate via wireless)
  Gateway is controlled remotely by third-party software

## Slide 6: Network Latency Varies Over Time
Round-trip times can vary by up to two orders of magnitude.
Is this caused by the access link or the home user?

## Slide 7: Network Latency Varies by User
Baseline Round-Trip Time Varies by about 20 milliseconds.
Homes about two blocks apart.

## Slide 8: One Approach: Netalyzr

## Slide 9: Netalyzr Data
130,000 runs of the system from 99,000 public IP addresses
Findings
  Over-buffering of links
  Inability to handle fragmentation
  Incorrectly operating Web caches
  Poor DNS performance

## Slide 10: System Design
Tradeoffs
  Flexibility for conducting a wide range of experiments
  Simple enough interface for users to run
Architecture

## Slide 11: Netalyzr Measurements
Network-layer Information
  IP Fragmentation
  Path MTU
  Latency, bandwidth, buffering
  IPv6 adoption
Service Reachability
DNS Measurements

## Slide 12: DNS Measurements
Check the acceptance of arbitrary A records
Check whether the server will follow CNAME
Server identification
  Resolver identity
  0x20 support
  Respect for short TTLs
  Whether the user’s NAT is proxying DNS

## Slide 13: HTTP Measurements
Proxy detection
Caching policies, transcoding, file-type blocking

## Slide 14: Results: Throughput

## Slide 15: Network-Layer Results
NATs are prevalent: 90% of all sessions
NAT often does not preserve the source port number for connections
Only 4.8% of sessions supported IPv6
Fragmentation not reliable: 8% no support
Buffering in DSL or DOCSIS cable modems
  250ms of additional latency during file transfers for 256 KB buffer, 8 Mbps up. >1 second for slower links.

## Slide 16: DNS Results
0x20 deployment is scarce
42% of sessions with a Linux-related user agent requested AAAA (IPv6) records
Prevalence of EDNS/DNSSEC resolvers
29% of resolvers had NXDOMAIN wildcarding

## Slide 17: ISP Policies

## Slide 18: NetPrints: Diagnosing Home Network Misconfigurations using Shared Knowledge
Bhavish Aggarwal, Ranjita Bhagwan, Tathagata Das, Venkat Padmanabhan Microsoft Research India
Siddharth Eswaran, IIT Delhi Geoff Voelker, UCSD
Notes: Need to change:
Add change tree/config trees
Add correct metric for mutation algorithm.
Add more on tree learning? C4.5 slide?

## Slide 19: Typical Home Network
Internet
IM
Email
Torrents
Browser
VPN client
Server
Email
IM
Game hosting
Multiplayer
No network admin!

## Slide 20: Examples of Problems
Problem | Solution
VPN client does not connect from home | Turn on PPTP passthrough on router, use a subnet that is either 192.168.0.x or 192.168.1.x
XBOX doesn’t connect to the Live service | Turn up your MTU above 1365, change NAT settings to full-cone, turn on UPnP
My IM client doesn’t work from home | Turn off the DNS proxy on the router
File sharing doesn’t seem to work at home | Make sure you and the file server are on the same domain/workgroup.
Printing doesn’t work from my laptop | Turn on correct firewall rules on print server machine
Cannot send large emails | Turn down MTU on your router
Diversity  home network troubleshooting is hard
Router misconfig
End-host
misconfig
Remote problem, local changes
Notes: Say “router” problem, “client” problem, “hidden configuration” … animate

## Slide 21: What Do Users Do Today?
Chart: 
| On-site service | Professional repair | New software | Friend/Family | Contacted ISP | Myself
 | 7 | 11 | 15 | 31 | 34 | 62
Avg time to resolve solutions: 2 hours
Source: Managing the Digital Home, a survey of 6,116 U.S. and Canadian home Internet users
© 2007 Parks Associates

## Slide 22: NetPrints
NetPrints = Network Problem Fingerprinting
Automate problem diagnosis using “shared knowledge”
NetPrints Service
Configuration info
Configuration info
Configuration info
Configuration info
Suggested changes
Notes: Netprints: network fingerprints?

## Slide 23: Putting NetPrints in Context
Windows Diagnostics Framework
Network Magic
Apple’s Diagnostics
Rule-based techniques
Strider+PeerPressure
Autobash
SVM-based performance debugger
Tracing, Learning-based
Resolve basic connectivity issues
(Application specific: too many rules)
Resolve local configuration issues
NetPrints
Distributed configuration information
Unstructured, heterogeneous environment
Problems caused due to interaction of multiple configurations
Notes: Do not undersell … say what is new in netprints: configuration info is distributed, unstructured, interactions cause new problems, new learning techniques. Add stuff to the slide

## Slide 24: Assumptions
Current design requires basic connectivity
  Looking at application-specific problems
  Not inherent, Knowledgebase can be shipped offline
Not dealing with performance
  “good” and “bad” are the only two states considered

## Slide 25: NetPrints in Action
NetPrints
server
Config.xml
…
pptp_pass=0
…
Suggest.xml
pptp_pass=1
Knowledgebase for VPN client
Notes: Add labs, arrow animations

## Slide 26: Diagnosis Strategies
Snapshot-based
  Collect config snapshots from different users
Change-based
  Collect config changes that a user makes
Symptom-based
  Collect signatures of problems from network traffic

## Slide 27: System Design
Local-Area
Network
Network Feature Extractor
Internet
Config
Scraper
(End-host
& Router)
Diagnosis engine
NetPrints Client
NetPrints Server
Internet Gateway Device
Change trees
Config trees
Sig-
natures
Server Knowledgebase
GUI
Notes: Change colour scheme (remove 3d)

## Slide 28: Normal Mode
GUI
Local-Area
Network
Network Feature Extractor
Internet
Config
Scraper
(End-host
& Router)
Diagnosis engine
NetPrints Client
NetPrints Server
Internet Gateway Device
1. Config
Scraper
(End-host
& Router)
Change trees
Config trees
Sig-
natures
Server Knowledgebase
4. Send data to server
2. Network Feature Extractor
Change trees
Config trees
Sig-
natures
5. Server Knowledgebase
GUI
3. GUI
Notes: Change colour scheme (remove 3d)

## Slide 29: Diagnose Mode
GUI
Local-Area
Network
Network Feature Extractor
Internet
Config
Scraper
(End-host
& Router)
Diagnosis engine
NetPrints Client
NetPrints Server
Internet Gateway Device
2. Config
Scraper
(End-host
& Router)
Change trees
Config trees
Sig-
natures
Server Knowledgebase
4. Send data to server
3. Network Feature Extractor
Change trees
Config trees
Sig-
natures
Server Knowledgebase
GUI
1. GUI
5. Diagnosis engine uses configuration mutation
Notes: Change colour scheme (remove 3d)

## Slide 30: #1: Configuration Scraper
Router scraper
  UPnP
  Web Interface (HTTP Request Hijacking)
End-host scraper
  Interface-specific parameters
  Patches and software versions
  Firewall rules
Remote scraper
  Composition of local and remote configs

## Slide 31: Composing Local & Remote Configs
Problem | Solution
VPN client does not connect from home | Turn on PPTP passthrough on router, use a subnet that is either 192.168.0.x or 192.168.1.x
XBOX doesn’t connect to the Live service | Turn up your MTU above 1365, change NAT settings to full-cone, turn on UPnP
My IM client doesn’t work from home | Turn off the DNS proxy on the router
File sharing doesn’t seem to work at home | Make sure client and the server are on the same domain/workgroup.
Printing doesn’t work from my laptop | Turn on correct firewall rules on print server machine
Cannot send large emails | Turn down MTU on your router
Sometimes it is the combination of local and remote configs that is the problem
Notes: Comparison engine ?

## Slide 32: #2: Server Knowledgebase
Per-application decision trees constructed using labeled configuration snapshots
  decision trees aid interpretability
  C4.5 decision tree learning algorithm
Configuration tree, Change trees and network signatures

## Slide 33: Methodology
Testbed comprising 7 different routers
  various makes: Netgear, Linksys, D-Link, Belkin
Clients running the VPN sent configurations to the NetPrints service
  Roughly 6000 config parameters per snapshot
Service learned configuration trees using C4.5 algorithm

## Slide 34: Example of Configuration Tree
pptp_pass
device
device
disable_spi
good
bad
bad
good
disable_spi
good
bad
0
1
Netgear
Linksys
Netgear
Linksys
0
1
0
1
Simplified Config Tree for VPN Client
Notes: Lookup ndf helper class… who calls what?

## Slide 35: Configuration Tree for VPN Client
local.disable_spi
Good (50/1)
Bad (48/0)
1
0
local.pptp_pass
NA
Good (49/0)
1
Good
(73/0)
NA
local.filter
0
Bad
(12/0)
NA
Bad
(54/0)
on
local.ethernet.speed
off
1Gbps
100Mbps
local.dmz_enable
Good
(42/0)
Good
(4/0)
1
local.ipsec_pass
Bad
(4/0)
0
local.l2tp_pass
1
0
Bad
(2/0)
Good
(2/0)
0
1

## Slide 36: #3: Configuration Mutation
pptp_pass
device
device
disable_spi
good
bad
bad
good
disable_spi
good
bad
0
1
Netgear
Linksys
Netgear
Linksys
0
1
0
1
1000
10
10
2000
2000
Preference for mutations involving frequently changing parameters
Assumption: higher the frequency, less disruptive the change
Track change frequency.
device=Linksys
pptp_pass=0
Notes: Write the algorithm better. Press the better button.

## Slide 37: Shortcoming of Configuration Trees
Some config info may not be learned
So traversal of config tree may end in a “good” leaf even if config is problematic
Reasons:
  Insufficient data
    e.g., a new router enters the market
  Hidden configurations
    e.g., application-specific parameters
Notes: Talk about only one hidden conf

## Slide 38: Summary of Diagnosis Procedure
Network traffic signature | Change trees
1 X X X X X X | 
0 X X X X 1 X | 
Configuration tree
Notes: Rearrange slide 20 and 19.

## Slide 39: Experimental Evaluation
Testbed comprising 7 different routers
  various makes: Netgear, Linksys, D-Link, Belkin
Internet
VPN Server
VPN Client
HOME
Internet
FTP Client
FTP Server
HOME
Internet
File Share
File Share
HOME

## Slide 40: Findings
Intuitive inferences
  VPN: If pptp_pass==1 then GOOD
Surprising inferences
  VPN: If stateful==off and pptp_pass==0 and ipsec_pass==0 and l2tp_pass==0 then GOOD

## Slide 41: Tolerance to Mislabeling
  13-17% mislabeling  1% error in diagnosis

## Slide 42: Tolerance to Mislabeling
  13-17% mislabeling  1% error in diagnosis

## Slide 43: Summary
Home network diagnostics is challenging
  diversity of apps and configs
  absence of an admin
NetPrints leverages community info to perform automated diagnosis
  decision tree based learning
  configuration trees, network traffic signatures and change trees
Notes: Get prototype to a working state … say that they asked for code by november.