## Slide 1: The Control Plane
Nick Feamster CS 6250: Computer Networks Fall 2011

## Slide 2: What is the Control Plane?
Essentially the “brain” of the network
Responsible for computing and implementing
  End-to-end paths (Routing)
  Permissions (Access Control Lists)
Today: The “Internet control plane” as we know it
  Layer 2 Path Computation: Spanning Tree
  Intradomain routing: OSPF/ISIS
  Interdomain routing: BGP
Question: Where should the control plane reside?

## Slide 3: Layer 2 Route Computation

## Slide 4: Life of a Packet: On a Subnet
Packet destined for outgoing IP address arrives at network interface
  Packet must be encapsulated into a frame with the destination MAC address
Frame is sent on LAN segment to all hosts
Hosts check destination MAC address against MAC address that was destination IP address of the packet

## Slide 5: Interconnecting LANs
Receive & broadcast (“hub”)
Learning switches
Spanning tree (RSTP, MSTP, etc.) protocols

## Slide 6: Interconnecting LANs with Hubs
All packets seen everywhere
  Lots of flooding, chances for collision
Can’t interconnect LANs with heterogeneous media (e.g., Ethernets of different speeds)
hub
hub
hub
hub

## Slide 7: Problems with Hubs: No Isolation
Scalability
Latency
  Avoiding collisions requires backoff
  Possible for a single host to hog the medium
Failures
  One misconfigured device can cause problems for every other device on the LAN

## Slide 8: Improving on Hubs: Switches
Link-layer
  Stores and forwards Ethernet frames
  Examines frame header and selectively forwards frame based on MAC dest address
  When frame is to be forwarded on segment, uses CSMA/CD to access segment
Transparent
  Hosts are unaware of presence of switches
Plug-and-play, self-learning
  Switches do not need to be configured

## Slide 9: Switch: Traffic Isolation
Switch breaks subnet into LAN segments
Switch filters packets
  Same-LAN-segment frames not usually forwarded onto other LAN segments
  Segments become separate collision domains
hub
hub
hub
switch
collision domain
collision domain
collision domain

## Slide 10: Filtering and Forwarding
Occurs through switch table
Suppose a packet arrives destined for node with MAC address x from interface A
  If MAC address not in table, flood (act like a hub)
  If MAC address maps to A, do nothing (packet destined for same LAN segment)
  If MAC address maps to another interface, forward
How does this table get configured?
LAN A
LAN B
LAN C
A
B
C

## Slide 11: Advantages vs. Hubs
Better scaling
  Separate collision domains allow longer distances
Better privacy
  Hosts can “snoop” the traffic traversing their segment
  … but not all the rest of the traffic
Heterogeneity
  Joins segments using different technologies

## Slide 12: Disadvantages vs. Hubs
Delay in forwarding frames
  Bridge/switch must receive and parse the frame
  … and perform a look-up to decide where to forward
  Storing and forwarding the packet introduces delay
  Solution: cut-through switching
Need to learn where to forward frames
  Bridge/switch needs to construct a forwarding table
  Ideally, without intervention from network administrators
  Solution: self-learning

## Slide 13: Motivation For Self-Learning
Switches forward frames selectively
  Forward frames only on segments that need them
Switch table
  Maps destination MAC address to outgoing interface
  Goal: construct the switch table automatically
switch
A
B
C
D

## Slide 14: (Self)-Learning Bridges
Switch is initially empty
For each incoming frame, store
  The incoming interface from which the frame arrived
  The time at which that frame arrived
  Delete the entry if no frames with a particular source address arrive within a certain time
A
B
C
D
Switch learns how to reach A.

## Slide 15: Cut-Through Switching
Buffering a frame takes time
  Suppose L is the length of the frame
  And R is the transmission rate of the links
  Then, receiving the frame takes L/R time units
Buffering delay can be a high fraction of total delay, especially over short distances
A
B
switches

## Slide 16: Cut-Through Switching
Start transmitting as soon as possible
  Inspect the frame header and do the look-up
  If outgoing link is idle, start forwarding the frame
Overlapping transmissions
  Transmit the head of the packet via the outgoing link
  … while still receiving the tail via the incoming link
  Analogy: different folks crossing different intersections
A
B
switches

## Slide 17: Limitations on Topology
Switches sometimes need to broadcast frames
  Unfamiliar destination: Act like a hub
  Sending to broadcast
Flooding can lead to forwarding loops and broadcast storms
  E.g., if the network contains a cycle of switches
  Either accidentally, or by design for higher reliability
Worse yet, packets can be duplicated and proliferated!

## Slide 18: Solution: Spanning Trees
Ensure the topology has no loops
  Avoid using some of the links when flooding
  … to avoid forming a loop
Spanning tree
  Sub-graph that covers all vertices but contains no cycles
  Links not in the spanning tree do not forward frames

## Slide 19: Constructing a Spanning Tree
Elect a root
  The switch with the smallest identifier
Each switch identifies if its interface is on the shortest path from the root
  And it exclude from the tree if not
  Also exclude from tree if same distance, but higher identifier
Message Format: (Y, d, X)
  From node X
  Claiming Y as root
  Distance is d
root
One hop
Three hops

## Slide 20: Steps in Spanning Tree Algorithm
Initially, every switch announces itself as the root
  Example: switch X announces (X, 0, X)
Switches update their view of the root
  Upon receiving a message, check the root id
  If the new id is smaller, start viewing that switch as root
Switches compute their distance from the root
  Add 1 to the distance received from a neighbor
  Identify interfaces not on a shortest path to the root and exclude those ports from the spanning tree

## Slide 21: Example From Switch #4’s Viewpoint
Switch #4 thinks it is the root
  Sends (4, 0, 4) message to 2 and 7
Switch #4 hears from #2
  Receives (2, 0, 2) message from 2
  … and thinks that #2 is the root
  And realizes it is just one hop away
Switch #4 hears from #7
  Receives (2, 1, 7) from 7
  And realizes this is a longer path
  So, prefers its own one-hop path
  And removes 4-7 link from the tree
1
2
3
4
5
6
7

## Slide 22: Switches vs. Routers
Switches are automatically configuring
Forwarding tends to be quite fast, since packets only need to be processed through layer 2
Router-level topologies are not restricted to a spanning tree
  Can even have multipath routing
Switches
Routers

## Slide 23: Scaling Ethernet
Main limitation: Broadcast
  Spanning tree protocol messages
  ARP queries
High-level proposal: Distributed directory service
  Each switch implements a directory service
  Hosts register at each bridge
  Directory is replicated
  Queries answered locally
…are there other ways to do this?

## Slide 24: Intradomain Routing

## Slide 25: Routing Inside an AS
Intra-AS topology
  Nodes and edges
  Example: Abilene
Intradomain routing protocols
  Distance Vector
    Split-horizon/Poison-reverse
    Example: RIP
  Link State
    Example: OSPF, ISIS

## Slide 26: Topology Design
Where to place “nodes”?
  Typically in dense population centers
    Close to other providers (easier interconnection)
    Close to other customers (cheaper backhaul)
  Note: A “node” may in fact be a group of routers, located in a single city. Called a “Point-of-Presence” (PoP)
Where to place “edges”?
  Often constrained by location of fiber

## Slide 27: Example: Abilene Network Topology

## Slide 28: Where’s Georgia Tech?
10GigE (10GbpS uplink) Southeast Exchange
(SOX) is at 56 Marietta Street

## Slide 29: Intradomain Routing: Two Approaches
Routing: the process by which nodes discover where to forward traffic so that it reaches a certain node
Within an AS: there are two “styles”
  Distance vector: iterative, asynchronous, distributed
  Link State: global information, centralized algorithm

## Slide 30: Forwarding vs. Routing
Forwarding: data plane
  Directing a data packet to an outgoing link
  Individual router using a forwarding table
Routing: control plane
  Computing paths the packets will follow
  Routers talking amongst themselves
  Individual router creating a forwarding table

## Slide 31: Distance Vector Algorithm
Iterative, asynchronous: each local iteration caused by:
Local link cost change
Distance vector update message from neighbor
Distributed:
Each node notifies neighbors only when its DV changes
Neighbors then notify their neighbors if necessary
wait for (change in local link cost or message from neighbor)
recompute estimates
if DV to any destination has changed, notify neighbors
Each node:

## Slide 32: Link-State Routing
Keep track of the state of incident links
  Whether the link is up or down
  The cost on the link
Broadcast the link state
  Every router has a complete view of the graph
Compute Dijkstra’s algorithm
Examples:
  Open Shortest Path First (OSPF)
  Intermediate System – Intermediate System (IS-IS)

## Slide 33: Link-State Routing
Idea: distribute a network map
Each node performs shortest path (SPF) computation between itself and all other nodes
Initialization step
  Add costs of immediate neighbors, D(v), else infinite
  Flood costs c(u,v) to neighbors, N
For some D(w) that is not in N
  D(v) = min( c(u,w) + D(w), D(v) )

## Slide 34: Detecting Topology Changes
Beaconing
  Periodic “hello” messages in both directions
  Detect a failure after a few missed “hellos”
Performance trade-offs
  Detection speed
  Overhead on link bandwidth and CPU
  Likelihood of false detection
“hello”

## Slide 35: Broadcasting the Link State
Flooding
  Node sends link-state information out its links
  The next node sends out all of its links except the one where the information arrived
X
A
C
B
D
(a)
X
A
C
B
D
(b)
X
A
C
B
D
(c)
X
A
C
B
D
(d)

## Slide 36: Broadcasting the Link State
Reliable flooding
  Ensure all nodes receive the latestlink-state information
Challenges
  Packet loss
  Out-of-order arrival
Solutions
  Acknowledgments and retransmissions
  Sequence numbers
  Time-to-live for each packet

## Slide 37: When to Initiate Flooding
Topology change
  Link or node failure
  Link or node recovery
Configuration change
  Link cost change
Periodically
  Refresh the link-state information
  Typically (say) 30 minutes
  Corrects for possible corruption of the data

## Slide 38: Scaling Link-State Routing
Message overhead
  Suppose a link fails. How many LSAs will be flooded to each router in the network?
    Two routers send LSA to A adjacent routers
    Each of A routers sends to A adjacent routers
    …
  Suppose a router fails. How many LSAs will be generated?
    Each of A adjacent routers originates an LSA …

## Slide 39: Scaling Link-State Routing
Two scaling problems
  Message overhead: Flooding link-state packets
  Computation: Running Dijkstra’s shortest-path algorithm
Introducing hierarchy through “areas”
Area 0
area
border
router

## Slide 40: Link-State vs. Distance-Vector
Convergence
  DV has count-to-infinity
  DV often converges slowly (minutes)
  DV has timing dependences
  Link-state: O(n2) algorithm requires O(nE) messages
Robustness
  Route calculations a bit more robust under link-state
  DV algorithms can advertise incorrect least-cost paths
  In DV, errors can propagate (nodes use each others tables)
Bandwidth Consumption for Messages
  Messages flooded in link state

## Slide 41: Open Shortest Paths First (OSPF)
Key Feature: hierarchy
Network’s routers divided into areas
Backbone area is area 0
Area 0 routers perform SPF computation
  All inter-area traffic travles through Area 0 routers (“border routers”)
Area 0

## Slide 42: Another Example: IS-IS
Originally: ISO Connectionless Network Protocol
  CLNP: ISO equivalent to IP for datagram delivery services
  ISO 10589 or RFC 1142
Later: Integrated or Dual IS-IS (RFC 1195)
  IS-IS adapted for IP
  Doesn’t use IP to carry routing messages
OSPF more widely used in enterprise, IS-IS in large service providers

## Slide 43: Hierarchical Routing in IS-IS
Area 49.001
Area 49.0002
Level-1
Routing
Level-2
Routing
Level-1
Routing
Backbone
Like OSPF, 2-level routing hierarchy
  Within an area: level-1
  Between areas: level-2
  Level 1-2 Routers: Level-2 routers may also participate in L1 routing

## Slide 44: ISIS on the Wire…

## Slide 45: Interdomain Routing
See http://nms.lcs.mit.edu/~feamster/papers/dissertation.pdf (Chapter 2.1-2.3) for good coverage of today’s topics.

## Slide 46: Internet Routing
Large-scale: Thousands of autonomous networks
Self-interest: Independent economic and performance objectives
But, must cooperate for global connectivity
Comcast
Abilene
AT&T
Cogent
Georgia
Tech
The Internet

## Slide 47: Internet Routing Protocol: BGP
Route Advertisement
Autonomous Systems (ASes)
Session
Traffic
Destination Next-hop AS Path
130.207.0.0/16
130.207.0.0/16
192.5.89.89
66.250.252.44
10578..2637
174… 2637
Notes: Diagram of routing table is very confusing because it’s not pointing to anything
Green arrow shorter, and too thick… green is a msg
More intuition about how the system actually works.
Don’t say “interdomain”
DESTINATION-BASED Routing
Tables look like a set of possible routes and a rankings over these routes
(pop up a simplified table fragment)

## Slide 48: Two Flavors of BGP
External BGP (eBGP): exchanging routes between ASes
Internal BGP (iBGP): disseminating routes to external destinations among the routers within an AS
eBGP
iBGP
Question: What’s the difference between IGP and iBGP?

## Slide 49: Example BGP Routing Table
> show ip bgp
Network Next Hop Metric LocPrf Weight Path
*>i3.0.0.0 4.79.2.1 0 110 0 3356 701 703 80 i
*>i4.0.0.0 4.79.2.1 0 110 0 3356 i
*>i4.21.254.0/23 208.30.223.5 49 110 0 1239 1299 10355 10355 i
* i4.23.84.0/22 208.30.223.5 112 110 0 1239 6461 20171 i
The full routing table
> show ip bgp 130.207.7.237
BGP routing table entry for 130.207.0.0/16
Paths: (1 available, best #1, table Default-IP-Routing-Table)
Not advertised to any peer
10578 11537 10490 2637
192.5.89.89 from 18.168.0.27 (66.250.252.45)
Origin IGP, metric 0, localpref 150, valid, internal, best
Community: 10578:700 11537:950
Last update: Sat Jan 14 04:45:09 2006
Specific entry. Can do longest prefix lookup:
Prefix
AS path
Next-hop

## Slide 50: Routing Attributes and Route Selection
Local preference: numerical value assigned by routing policy. Higher values are more preferred.
AS path length: number of AS-level hops in the path
Multiple exit discriminator (“MED”): allows one AS to specify that one exit point is more preferred than another. Lower values are more preferred.
eBGP over iBGP
Shortest IGP path cost to next hop: implements “hot potato” routing
Router ID tiebreak: arbitrary tiebreak, since only a single “best” route can be selected
BGP routes have the following attributes, on which the route selection process is based:

## Slide 51: Other BGP Attributes
Next-hop: IP address to send packets en route to destination. (Question: How to ensure that the next-hop IP address is reachable?)
Community value: Semantically meaningless. Used for passing around “signals” and labelling routes. More in a bit.
Next-hop: 4.79.2.1
iBGP
4.79.2.1
4.79.2.2
Next-hop: 192.5.89.89

## Slide 52: Local Preference
Control over outbound traffic
Not transitive across ASes
Coarse hammer to implement route preference
Useful for preferring routes from one AS over another (e.g., primary-backup semantics)
Primary
Backup
Higher local pref
Lower local pref
Destination

## Slide 53: Communities and Local Preference
Customer expresses provider that a link is a backup
Affords some control over inbound traffic
More on multihoming, traffic engineering in Lecture 7
Primary
Backup
“Backup” Community
Destination

## Slide 54: AS Path Length
Among routes with highest local preference, select route with shortest AS path length
Shortest AS path != shortest path, for any interpretation of “shortest path”
Destination
Traffic

## Slide 55: Hot-Potato Routing
Prefer route with shorter IGP path cost to next-hop
Idea: traffic leaves AS as quickly as possible
I
New York
Atlanta
Washington, DC
5
10
Dest.
Common practice: Set IGP weights in accordance with propagation delay (e.g., miles, etc.)
Traffic

## Slide 56: Problems with Hot-Potato Routing
Small changes in IGP weights can cause large traffic shifts
I
San Fran
New York
LA
5
10
Dest.
Question: Cost of sub-optimal exit vs. cost of large traffic shifts
Traffic
11

## Slide 57: Internet Business Model (Simplified)
Customer/Provider: One AS pays another for reachability to some set of destinations
“Settlement-free” Peering: Bartering. Two ASes exchange routes with one another.
Provider
Peer
Customer
Preferences implemented with local preference manipulation
Destination
Pay to use
Get paid to use
Free to use

## Slide 58: A Clean Slate 4D Approach to Internet Control and Management

## Slide 59: Layers of the 4D Architecture
Data Plane:
Spatially distributed routers/switches
Can deploy with today’s technology
Looking at ways to unify forwarding paradigms across technologies
Decision
Dissemination
Discovery
Data
Network-level objectives
Direct control
Network-wide views

## Slide 60: Advantages of 4D
Separate network logic from distributed systems issues
  enables the use of existing distributed systems techniques and protocols to solve non-networking issues
Higher robustness
  raises level of abstraction for managing the network
  allows operators to focus on specific network-level objectives
Better security
  reduces likelihood of configuration mistakes
Accommodating heterogeneity
Enable Innovations
  only decision plane needs to be changed

## Slide 61: Challenges of 4D
Reducing complexity
  Dramatically simplifying overall system? Or is it just moving complexity?
Unavoidable delays to have network-wide view.
  Is it possible to have a network-wide view sufficiently accurate and stable to manage the network?
The logic is centralized in Decision Element (DE)
  Is it possible to respond to network failures and restore data flow within an acceptable time?
  DE can be a single point of failure.
  Attackers can compromise the whole network by controlling DE

## Slide 62: Research Agenda: Decision Plane
Algorithms to satisfy Network-level objectives
  Traffic Engineering: beyond intractable problems?
  Reachability Policies
  Planned Maintenance
  Specification of network-level objectives: new language?
Coordination between Decision Elements
  To avoid a single point of failure, multiple DE’s
  1) only elected leader sends instructions to all
  2) independent DE’s without coordination: network elements resolves commands from different DE’s
Hierarchy in Decision Plane

## Slide 63: Research Agenda: Dissemination Plane
Separate control from data “logically”
  supervisory channel in SONET, optical links
  no separation channel for control and data in the Internet
How to achieve robust, efficient connection of DE with routers and switches?
  flooding
  spanning-tree protocols
  source routing
When to apply the new logic in data plane
  each router applies update ASAP
  coordinate update at a pre-specified time: need time synch

## Slide 64: Research Agenda: Discovery Plane
Today
  consistency between management logic, configuration files, and physical reality is maintained manually!
4D
  Bootstrapping with zero pre-configuration
  Automatically discovering the identities of devices and the logical/physical relationships between them
  Supporting cross-layer auto-discovery

## Slide 65: Research Agenda: Data Plane
Data plane handles data packets under direct control of the decision plane
Decision plane algorithms should vary depending on the forwarding paradigms in data plane
Packet-forwarding paradigms
  Longest-prefix matching (IPv4, IPv6)
  Exact-match forwarding (Ethernet)
  Label switching (MPLS, ATM, Frame Relay)
Weighted splitting over multiple outgoing links or single out-going link?

## Slide 66: End-to-End Routing Behavior on the Internet

## Slide 67: End-to-End Routing Behavior
Importance of paper
  Revitalized field of network measurement
  Use of statistical techniques to capture new types of measurements
  Empirical findings of routing behavior (motivation for future work)
Various routing pathologies
  Routing loops
  Erroneous
  Connectivity altered mid-stream
  Fluttering…

## Slide 68: End-to-End Routing Behavior
Pathology
type
Prevalence
in 1995
Prevalence
in 1996
Long-lived
Routing loops
Short-lived
Routing loops
Outage>30s
Total
0.065%
~
0.14%
~
same
same
0.96%
2.2%
3.4%
1.5%

## Slide 69: Routing Loops
Persistent Routing Loops
  10 persistent routing loops in D1
  50 persistent routing loops in D2
Temporary Routing Loops
  2 loops in D1
  21 in D2
Location of Routing Loops: All in one AS

## Slide 70: Erroneous and Transient Routing
Transatlantic route to London via Israel!
Connectivity altered mid-stream
  10 cases in D1
  155 cases in D2
Fluttering: Packets to the same flow changing mid-stream

## Slide 71: Routing Prevalence and Persistence
Prevalence: How often is the route present in the routing tables?
  Internet paths are strongly dominated by a single route
Persistence: How long do routes endure before changing?
  Routing changes occur over a variety of time scales